## Slide 1
Automated Parking
Lot System
A smart microcontroller-based entry and exit gate management solution powered by ATmega32 AVR.
Team Team 4 — Embedded_Elite
Supervisor Eng. Hesham Ahmed
Microcontroller ATmega32 (8-Bit AVR @ 8MHz)
Course Embedded Systems Diploma

## Slide 2
System Concept & Simple Workflow
Key System Logic
If the parking lot reaches maximum capacity (Full), the Red LED illuminates, LCD displays "PARKING FULL", and entry requests are instantly rejected until a car exits (INT1 trigger).
Car Arrives
Vehicle triggers the entry sensor (External Interrupt INT0).
Check Spots
System checks if available parking spaces > 0 on LCD.
Enter PIN
Driver enters admin security passcode via 4x4 Keypad.
Gate Opens
Timer1 PWM moves Servo Motor to 90° for entry.
Log & Close
Counter updates, UART logs event, gate safely closes.

## Slide 3
Layered Software Architecture
Includes Modular Common Utilities: STD_TYPES.h, BIT_MATH.h, and Common_Macros.h.
APP Layer
High-level business logic controlling state transitions:
HAL Layer
Hardware Abstraction Drivers for peripherals:
MCAL Layer
Direct register-level AVR peripheral drivers:
•
Parking Manager State Machine
•
Spot Counter & Vehicle Manager
•
Security Password Verification
•
LCD 16x2 Display Driver
•
4x4 Matrix Keypad Driver
•
SG90 Servo Motor Driver
•
LED & Button Drivers
•
DIO Driver (Digital Inputs/Outputs)
•
EXTI Driver (External Interrupts)
•
TIMER1 Driver (16-bit Fast PWM)
•
UART Driver (Serial Logging)

## Slide 4
Main Hardware Components
ATmega32 MCU
Main 8-bit AVR microcontroller running at 8MHz, executing core logic & peripheral timing.
LCD Display 16x2
Real-time user interface showing available parking spots, system status & passcode prompts.
4x4 Matrix Keypad
Security passcode input for driver authentication & admin system maintenance mode.
SG90 Servo Motors
Controls physical entry & exit gate barriers via Timer1 Fast PWM signal generation.

## Slide 5
Proteus Schematic Simulation
Pin Interfacing
•
PORTA (PA0-PA7): LCD 8-bit Data Bus
•
PORTB (PB0-PB2): LCD Control (RS, RW, EN)
•
PORTC (PC0-PC7): 4x4 Matrix Keypad Rows/Cols
•
PORTD (PD2, PD3): Entry (INT0) & Exit (INT1) Sensors
•
PORTD (PD5, PD6): Timer1 PWM Servo Gates
•
PORTD (PD0, PD1): UART Virtual Terminal

## Slide 6
Member Work: Abdulrahman Ali Abdelaziz
Discusses: System Architecture, State Machine & Keypad Security Logic
Key Project Contributions
Abdulrahman Ali Abdelaziz Ali
TEAM LEADER & MCAL/HAL DEVELOPER
Project Architecture & APP Layer: Designed overall state machine logic (INIT, IDLE, ENTRY, EXIT, FULL, ADMIN).
DIO Driver: Implemented low-level Digital Input/Output port manipulation functions.
Keypad Driver: Developed matrix scan routine for security passcode verification.
Integration & Testing: Led GitHub repository management, Proteus simulation assembly, and hardware debugging.
LCD Driver: Wrote 16x2 character LCD driver in 8-bit mode for displaying live counter & user messages.

## Slide 7
Member Work: Yousef Mohamed Al-Sayed
Discusses: External Interrupts (INT0/INT1), LED Indicators & Vehicle Sensing
Key Project Contributions
Yousef Mohamed Al-Sayed Abohashem
MCAL / HAL DEVELOPER
EXTI Driver: Configured External Interrupts (INT0, INT1) for instant vehicle detection without blocking MCU execution.
LED Driver: Developed visual status indicators (Green for Space Available, Red for Parking Full).
APP Layer Support: Assisted in vehicle entry/exit counter calculations & condition checking.
Hardware Simulation: Validated interrupt edge triggers and LED state toggles in Proteus.

## Slide 8
Member Work: Omar Hamdy Hamed
Discusses: LCD Display Interface & Real-time UART Event Logging
Key Project Contributions
Omar Hamdy Hamed Abdelrahman
HAL & COMMUNICATION DEVELOPER
UART Driver: Implemented serial communication driver to transmit real-time system log events to Virtual Terminal.
Event Logging: Configured event strings (e.g., "ENTRY GATE OPENED", "PARKING FULL").
Presentation: Co-created presentation materials and system documentation.

## Slide 9
Member Work: Omar Alaa Eldin
Discusses: 16-bit Timer1, Fast PWM Generation & Timing Calculations
Key Project Contributions
Omar Alaa Eldin Abdelrady
MCAL DEVELOPER
Timer1 MCAL Driver: Programmed ATmega32 16-bit Timer1 peripheral in Fast PWM Mode (Mode 14).
PWM Generation: Generated precise 50Hz PWM signals required for standard servo motor positioning.
Prescaler & ICR1 Setup: Calculated exact ICR1 top value for 20ms period (50Hz) at 8MHz clock frequency.
Presentation: Co-created technical slides and hardware timing diagrams.

## Slide 10
Member Work: Mina Ramy Rizk
Discusses: SG90 Servo Actuation & Gate Angle Duty Cycle Mapping
Key Project Contributions
Mina Ramy Rizk Youssef
HAL DEVELOPER & SIMULATION ENGINEER
Servo Motor HAL Driver: Created high-level API functions SERVO_voidSetAngle() mapping 0° to 180° angles.
Gate Motion Logic: Calibrated Duty Cycle pulse widths (1ms for 0° closed, 1.5ms for 90° open).
Proteus Simulation: Designed and tested servo motor response during entry and exit gate routines.
Presentation: Contributed to presentation visual materials and system demonstration.

## Slide 11
Embedded_Elite
ATmega32 AVR
Thank You!
The Automated Parking Lot System successfully demonstrates modular layered software architecture and real-time embedded control on ATmega32.
Questions & Discussion